## Slide 1
Exercise 3a: Calibration
Peter Burek, Carla Catania, Silvia Artuso International Institute for Applied Systems Analysis
Water Security Group

## Slide 2: Calibration
0. What you need
1. Introduction into calibration
3. A fast calibration
4. Visualization of the results
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 3: Calibration
0. What you need
• Python 3.7 - 3.12
CWatM running as python version
• additional library: deap pip install deap (or conda install deap)
• and the library: matplotlib
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 4: Calibration
Finding a parameter set which represents the observed discharge data
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 5: Calibration CWatM Parameters
13 parameters are calibrated:
Snow
Snowfactor as a factor to amount of snow
SnowMelt: day-degree factor how much snow is melted per ℃
Evapotranspiration
3. Crop factor as an adjustment to crop evapotranspiration
Soil
4. ksatfactor: a factor for the conductivity of soil of soil layer 1 and 2
5. soilfactor: a factor to the depth of soil layer 2
6. Preferential bypass flow: empirical shape parameter of the preferential flow relation
7. Infiltration capacity parameter: empirical shape parameter b of the ARNO model
Groundwater
8. Interflow factor: factor to adjust the amount which percolates from interflow to groundwater
9. Recession coefficient: how fast is groundwater translated into baseflow
Routing
10. Runoff concentration: how fast is the runoff at the outlet of a grid cell
11. Channel Manning’s n factor: a factor roughness in channel routing
Reservoir & lakes
12. Normal storage limit: the fraction of storage capacity used as normal storage limit
13. Lake A factor : factor to channel width and weir coefficient as a part of the Poleni weir equation
Parameter space for a calibration runs

## Slide 6: Calibration CWatM Objective function
Discharge:
Daily pairs of observed and simulated discharge at gauging stations
Objective function: Modified version of the Kling-Gupta Efficiency (Kling et al., 2012),
r as the correlation coefficient between simulated and observed discharge (dimensionless), β as the bias ratio (dimensionless) and γ as the variability ratio.
CV is the coefficient of variation, μ is the mean streamflow [m3 s−1] σ is the standard deviation of the streamflow [m3 s−1]. KGE’, r, β and γ have their optimum at 1.
Gupta, H. V., H. Kling, K. K. Yilmaz and G. F. Martinez (2009). “Decomposition of the mean squared error and NSE performance criteria: Implications for improving hydrological modelling.” Journal of Hydrology 377(1-2): 80-91
Kling, H., M. Fuchs and M. Paulin (2012). “Runoff conditions in the upper Danube basin under an ensemble of climate change scenarios.” Journal o Hydrology 424-425: 264-277

## Slide 7: Calibration CWatM on discharge Method
Calibration is using an evolutionary computation framework in Python called DEAP (Fortin et al., 2012).
DEAP implemented the evolutionary algorithm NSGA-II (Deb et al., 2002) which is used here as single objective optimization.
- Calibration start with an initial population size (µ)
- Each generation the best pool (λ) is selected and
recombined
- After a number of generation, the best fitting calibration is found
Félix-Antoine Fortin, François-Michel De Rainville, Marc-André Gardner, Marc Parizeau and Christian Gagné, “DEAP: Evolutionary Algorithms Made Easy”, Journal of Machine Learning Research, vol. 13, pp. 2171-2175
Deb, K., A. Pratap, S. Agarwal and T. Meyarivan (2002). “A fast and elitist multiobjective genetic algorithm: NSGA-II.” IEEE Transactions on Evolutionary Computation 6(2): 182-197.
Evolution of parameter space

## Slide 8: Calibration
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 9: Calibration
Upstream to downstream calibration
Morava basin with 21 subbasins
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 10: Calibration
Upstream to downstream calibration
Morava basin with 21 subbasins
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 11: Calibration
1.Running a fast calibration for an upstream basin
Go to your basin folder and /basin_calibration_tool
Correcting path in the settings files:
Settings1_fast.txt
Set the path name to your computer settings
Set this to: use_multiprocessing = 0
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 12: Calibration
1.Running a fast calibration for an upstream basin
Go to your basin folder and /basin_calibration_tool/templates
Correcting path in the settings files:
2) settings_morava_1min2.ini
Set the path name to your computer settings
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 13: Calibration
2.Running a fast calibration for an upstream basin
Go to your basin folder and /basin_calibration_tool/
Running a fast calibration
Execute: runsingle.bat or python calibration_single_single.py
This will launch a fast calibration in an upstream basin (here: G0022)
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 14: Calibration
2.Running a fast calibration for an upstream basin
The fast calibration is using only:
- Initial population of 4 (normally ≥ 256)
- 2 generations (normally ≥ 10)
- 2 runs per generation (normally ≥ 32)
Please stop the run
Change back:
Use_multiprocessing = 1
the calibration is splitting the runs for multiprocessing
Run again: runsingle.bat
Settings1_fast.txt – last part
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 15: Calibration
2.Running a fast calibration for an upstream basin
The fast calibration is using only:
- Initial population of 4 (normally ≥ 256)
- 2 generations (normally ≥ 10)
- 2 runs per generation (normally ≥ 32)
Please stop the run
Change back:
Use_multiprocessing = 1
the calibration is splitting the runs for multiprocessing
Run again: runsingle.bat
Folder structure in:
morava_calibration_tool\calibration1\G0022\out
at start:
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 16: Calibration
3. Look at the results
Your DOS box should look like this
After the calibration, the subbasin is run again for a greater time period
Folder structure in:
morava_calibration_tool\calibration1\G0022\out
at end of the calibration:
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 17: Calibration
3. Look at the results
Execute: runC10.bat or python CAL_10_COMPUTE_STATS_AND_FIGURES_TIME_SERIES.py settings1_fast.txt
To create a figure in:
yourbasin_calibration_tool\calibration1\FIGURES
This is the single basin calibration:
For a “real calibration” you have to change the [DEAP] parameter in settings1_fast
G0022_Morava_Velka_Bystrice_.png
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 18: Calibration
4. Some more information
Calibration1: has the results for different subbasin in the beginning it should have only inflow, maps, out
cwatm: A copy of the model
ListPC: This has a list of subbasin. If you run top to downstream calibration with several computer: it tells each computer what is done, what is running
Observed_data: Has the metadata and the discharge timeseries of subbasin stations
Result,staticdata,temp: Some folders to store some inbetween data
Templates: hold the settingsfile for calibration with placeholders: e.g. SnowMeltCoef = %snowmelt Placeholders are filled in during each calibration run
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 19: Calibration
4. Some more information
CAL_10_COMPUTE_STATS_AND_FIGURES_TIME_SERIES.py:
Tool to produce figures for each subbasin
calibration_main2.py: Prg to run a upstream to downstream calibration
calibration_single2e.py: Prg which is executed by calibration_main2.py for each subbasin. First the upstreams then working down
calibration_single_single.py:`Prg which runs a single basin. No of subbasin is hard coded del_cal1.py: Deletes all runs in calibration1
hydroStats.py Has all the objective functions
ParamRanges3.csv Here the parameter and thweir range are stored settings1_fast.txt: Settings_file for a single subbasin
settings1.txt: Settingsfile for a top-down calibration
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 20: Calibration
What can go wrong 1
Run runsingle.bat python calibration_single_single.py
Your python version is starting with python3 or you have to put in the full path of your python version c:/python38/python3 calibration_single_single.py
You did not change the path in settings file settings1_fast.txt and templates/settings_morava_1min2.ini
You did not download the meteo data from Sharepoint or you did not download other data
You still have problems with the gdal library
- use the newest version of CWatM on Sharepoint
- install gdal like in https://cwatm.iiasa.ac.at/setup.html#external-libraries
You have problems with white space in file names Use e.g. “c:/white space/python.exe” calibration_single_single.py
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 21: Calibration
What can go wrong 2
Run runsingle.bat python calibration_single_single.py
You did not add the libraries deap, matplotlib and pandas
Some results are already in basin/calibrationtool/calibration1/G0022 (or the G00?? You are using)
delete the files and the /out directory, make a new out directory
You cannot load the settings files, Your settings file are not stored as utf-8.
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 22: Calibration
1.What can go wrong 3
Run runsingle.bat python calibration_single_single.py
You run it but it crash:
Go to basin_calibration_tool/calibration1/G00??/out
Is there a folder 00_000?
No: bad, go back to what can go wrong 2
yes: good, go into 00_000
Inside 00_000 there is a file runpy00_000.bat
type cmd in the explorer to start a new DOS box
type runpy00_000.bat and execute
CWatm is running?
Yes: very good – check if the observed data in basin_calibration_tool \observed_data/ qgis_yourbasin_5.csv are in right format
No: change settings_fast-Run00_000.ini (e.g. path name) till CWatM is running copy the changes into templates/settings.ini
Please have a look at:
https://cwatm.iiasa.ac.at/calibration.html
https://cwatm.iiasa.ac.at/calibration_tutorial.html
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.